## Slide 1: Basic Electrical Engineering (BEEE101L)
Presented By
Dr. Maddela Chinna Obaiah
Assistant Professor (Sr)
School of Electrical Engineering

## Slide 2: Phasor Relationships for Circuit Elements
Resistor
Consider AC current
Voltage across it given by
The phasor form of this voltage is
The phasor form of current is
Hence,
time-domain
Phasor domain
Phasor Diagram
Current and voltage waveforms

## Slide 3: Inductor:
The phasor transform of derivative is
Consider AC current flowing through inductor
The voltage across the inductor is
It is becomes

## Slide 4: Capacitor:
The phasor transform of derivative is
Consider AC voltage across Capacitor, v
The current through the capacitor is
It is becomes

## Slide 5
Problem:
Problem:

## Slide 6: Impedance
As a complex quantity, the impedance may be expressed in rectangular and polar form as
where =resistance, and reactance
In a purely inductive circuit the opposition to the flow of alternating current is called the inductive reactance,
In a purely capacitive circuit the opposition to the flow of alternating current is called the capacitive reactance,

## Slide 7: R-L Series Circuit
From Phasor diagram (b)
(total opposition offered to the flow of alternating current by R-L series circuit is known as impedance of the circuit).

## Slide 8
The impedance triangle from phasor diagram (b) is shown in Fig. (c).
From impedance triangle,
From Fig. (d), it is evident that voltage leads the current by an angle such that

## Slide 9
Problem: A coil has a resistance of 4 and an inductance of 9.55mH. Calculate (a) the reactance, (b) the impedance, and (c) the current taken from a 240V, 50Hz supply. Determine also the phase angle between the supply voltage and current.
Solution: Given data
R=4; L =9.55mH=9.55×10−3H; f =50Hz; V =240V
Inductive reactance, XL =2πfL =2π(50)(9.55×10−3)=3
(b) Impedance, Z =√(R2 +XL2 )=√(42+32)=5
(c) Current, I = V/Z= 240/5=48A
The circuit and phasor diagrams and the voltage and impedance triangles are as shown in Figure.
Since tanφ= XL/R, φ= tan−1 (XL/R) = tan−1 (3/4) = 36.87◦ lagging

## Slide 10
Problem: A pure inductance of 1.273mH is connected in series with a pure resistance of 30. If the frequency of the sinusoidal supply is 5kHz and the p.d. across the 30 resistor is 6V, determine the value of the supply voltage and the voltage across the 1.273mH inductance. Draw the phasor diagram.
Solution: Given data
L=1.273mH, R=30 ohm, VR=6V, f=5kHz
Supply voltage, V =IZ
Current I = VR /R= 6/30=0.20A
Inductive reactance XL=2πfL=2π(5×103)(1.273×10−3)=40
Impedance, Z =√(R2 +XL2)=√(302+402)=50
Supply voltage V =IZ=(0.20)(50)=10V
Voltage across the 1.273mH inductance, VL=IXL=(0.2)(40)=8V
The phasor diagram is shown in Figure.
Fig. Phasor diagram

## Slide 11
Problem
Solution

## Slide 12
Problem
Solution

## Slide 13: R-C Series Circuit
From Phasor diagram (b)
(total opposition offered to the flow of alternating current by R-C series circuit is known as impedance of the circuit).

## Slide 14
The impedance triangle from phasor diagram (b) is shown in Fig. (c).
From impedance triangle,
From Fig. (d), it is evident that voltage leads the current by an angle such that
(d) I leads V by angle

## Slide 15
Problem: A resistor of 25 is connected in series with a capacitor of 45μF. Calculate (a) the impedance, and (b) the current taken from a 240V, 50Hz supply. Find also the phase angle between the supply voltage and the current.
Solution: Given date
R=25; C = 45μF = 45×10−6 F; V =240V; f =50Hz
Capacitive reactance, XC = 12πfC= 12π(50)(45×10−6)= 70.74
(a) Impedance Z =√(R2 +XC2)=√[(25)2+(70.74)2]=75.03
(b) Current I = V/Z= 240/75.03=3.20A
Phase angle between the supply voltage and current from impedance triangle,
α= tan−1(XC/R)
hence α= tan-1(70.7425)=70.54◦ leading

## Slide 16
Problem
Solution

## Slide 17: R-L-C Series Circuit

## Slide 18
When XL=XC (from (d)), the applied voltage V and the current I are in phase. This effect is called series resonance

## Slide 19
Problem
Solution

## Slide 20
Ans: Current I = 5.15 A, phase difference (lagging), Power consumed =371.1 W.
Problem: A 40μF capacitor in series with a coil of resistance 8 ohm and inductance 80mH is connected to a 200V, 100Hz supply. Calculate (a) the circuit impedance, (b) the current flowing, (c) the phase angle between voltage and current, (d) the voltage across the coil, and (e) the voltage across the capacitor.
Ans: (a) 13.18 (b) 15.17A (c) 52.63◦ lagging (d) 772.1V (e) 603.6V

## Slide 21: Resonance in RLC circuits